## Slide 1: Course Advanced SWAT Day 3
What did we learn yesterday?
Downloading MODIS data: not so easy
Calibrating GR4J with both satellite ET and flow
Setting up SWAT calibration in SWAT-CUP using PSO

## Slide 2: MODIS download
MODISTools no longer exist on CRAN
There are two other packages that need investigating:
  MODIStsp
  MODIS
  Both these packages are more about downloading raw data from what I can see now
MODISTools is still available on github and can be installed from there? https://github.com/seantuck12/MODISTools
Willem to investigate

## Slide 3: hydromad
Using earlier downloaded MODIS ET data, we can calculate the ET at every centroid of subbasins
  There are several assumptions about averaging and this needs recognition and further research
We demonstrated calibrating GR4J with satellite data on the Cotter
  Limited parameters and “lumped model” means that more data does not lead to better calibration
  However, does lead to forcing “correct” pattern in predicted ET
Developing a model for Santa Lucia was not yet done

## Slide 4: SWAT-CUP
SWAT-CUP is a bit involved to set up and takes considerable time to run the calibration (depends on CPU speed)
I have written a specialised R function that helps write the input for SWAT-CUP
We discussed the best way to calibrate a model with SWAT-CUP
  Set up sensitivity analysis using lots of parameters in a SUFI-2 model
  Run many simulations and inspect dotty plots and sensitivity
  From this select a maximum of 20 parameters (and check parameters that are important for considered processes)
  Use these parameters to set up a PSO calibration in SWAT-CUP

## Slide 5: What are we doing today
Continuing with SWAT-CUP, but demonstrating how we can include satellite data in the calibration
Setting up SWAT-CUP to calibrate a Santa Lucia,
If we have satellite data, with satellite data
Otherwise using nutrient data?