## Slide 1: Course Advanced SWAT Day 4
What did we learn yesterday?
Reformatting the precipitation data
More SWAT-CUP struggles
Santa Lucia catchment set-up in SWAT.

## Slide 2: Reformatting precipitation data
THIS IS ONLY FOR DIRECTLY REPLACING PCP1.PCP if you already have finished ARCSWAT/QSWAT setup
Quite involved
  SWAT only uses station closest to subbasin centroid
  Need to exclude stations with missing data?
  See updated script
  Script is generic: can be used for any number of stations and any number of subbasins (we will test this with Flora’s SWAT model)

## Slide 3: SWAT-CUP struggles
I didn’t really get to this, but here are some summaries
SWAT-CUP:
  Versatile, multiple objective functions and multiple optimisation routines, but program is not open source
  With respect to ET: cannot calibrate against accumulated values
  But you can put in “weighting” for different observed data
  Cannot calibrate on log transformed values, but can specify in file.cio that output is log(flow), ILOG = 1, then observed data should also be log(flow)
  Cannot calibrate on flow duration (flood frequency) curve
We started looking at running SWAT-CUP with ET as input for calibration

## Slide 4: SWAT-CUP and R
Describes what I wrote on the white board yesterday
Using the “SWAT-CUP functions”
  setwd()
  Source “Swatcupfunctions.R
  Copy original “observed_rch”, “observed_sub” and “observed” files from “PSO.in” or “SUFI2.in” folder to the working directory
  Run R script, if script fails, check script but also back to 3
  Check resulting files, if not right, check script, but also back to 3
  Copy paste content of files into SWAT-CUP window

## Slide 5: Santa Lucia SWAT-CUP
We have set up the Santa-Lucia SWAT model in SWAT-CUP as a SUFI-2
Discussed which parameters might be good to test
  Demonstrated how you can separate parameters by different landuse and soil hydrologic groups (see page 51 in SWAT-CUP manual)
It helps if you use the right reach (stream section) 

## Slide 6: What are we doing today
Continuing with SWAT-CUP, and using satellite data in the calibration
Setting up SWAT-CUP to calibrate a Santa Lucia, and include satellite data
Look at using nutrient data
Start on hydroPSO