## Slide 1: Course Advanced SWAT Day 5
What did we learn yesterday?
Lots and lots of SWAT-CUP
Demonstrated code for selecting rainfall data with fewer missing data
Short introduction in hydroPSO
Discussion about satellite data and the use in hydrological modelling

## Slide 2: Lots and lots of SWAT-CUP
We reviewed the Santa-Lucia SWAT model in SWAT-CUP as a SUFI-2
Identified errors in the definition of parameters for different groups.
  Demonstrated how you can separate parameters by different landuse and soil hydrologic groups (see page 51 in SWAT-CUP manual)
  Landuse needs 6 under scores not 4
Stepped through every file in the PSO.IN and showed how data is generated:
  For observed_rch.txt you need the R script to quickly generate the observed data. Make sure you check the input carfully
  See: 20170810_MorningSantaLuciaSWATCup.R

## Slide 3: Lots and lots of SWAT-CUP
Investigated the results of the SUFI2 to decide which parameters to include in the PSO optimisation
Set up PSO optimisation, analyse results today
Includes optimisation on Flow and ET
To do just “flow”: switch off “sub” and check pso_extract.bat
How to validate/evaluate
  Take “best pars” from calibration and put in to par_inf.txt
  Set par_inf.txt to 1 simulation and 1 iteration
  Generate new observed_rch.txt and observed.txt (and observed_sub.txt) using R script for a “validation period” (maybe 2005 – 2007)
  Clip and paste into SWAT-CUP files, run calibration (only 1 simulation) and analyse results

## Slide 4: Rainfall data
Script should be generic, Willem needs to test for subbasins from QSWAT from Flora
Now includes excluding rainfall stations with > 10% NA values
  Check with Willem when you want to use this script: not easy
  “SantaLuciaStationsToPCPFile.R” in functions folder
We also looked at CHIRPS, we need to learn how to download and use
Can compare to observed data, satellite data and station data were used to develop data set.

## Slide 5: Miscellaneous
We discussed satellite data more general and what can be useful in hydrological modelling
Willem’s opinion:
  The main strength in satellites is in landscape energy balance
  Most satellites have just colour bands and infrared
  Microwave for soil moisture: trade-off spatial scale and depth of penetration: large spatial, deeper penetration, small spatial, shallow penetration.
  For hydrology: deep soil moisture is more important
  For climate: shallow soil moisture
  Water quality: Lakes and oceans, not sure about rivers (apart from very big rivers)
  Can observe flooding

## Slide 6: What are we doing today
How to extract and plot results from SWAT-CUP with R
hydroPSO set-up Santa Lucia
  Run small example
Discussion and questions
To do list Willem
  Santa Lucia nutrient and multiple flow stations example
  New handout/test MODISTools or MODIStsp
  Extract CHIRPS
  Better handout HPC Sydney for hydroPSO
  Old teaching material: landuse change: on drive
  “cheat sheet” Validation/Evaluation

## Slide 7: To do list Willem
Santa Lucia nutrient and multiple flow stations example
New handout/test MODISTools or MODIStsp
Extract CHIRPS
Get hydroPSO to work for SantaLucia
  Split parameters by subbasin, land use and soil type
Better handout HPC Sydney for hydroPSO
Old teaching material: landuse change: on drive
“cheat sheet” Validation/Evaluation